## Slide 1: Retro Tv Project
By: Haidar Ali Alshowaikh
Class: 8E

## Slide 2: Matirials Used:
1- Rassperi Pi
2-Arduino Uno
3-Potentiometer 10K (A Knob)
4-Jumper Wires (Male to Female, and Female to Female)
5-Button
6-Joystick Module
7-A old Laptop screen
8- hdmi module

## Slide 3: The Idea 01 The Problems 02 Solution of Problems 03 The Wirring 04 Goals 05
How I got the idea
The problems I faced during this project
How I solved these problems
How I wired the parts to the board
What are my project’s goals.

## Slide 4: The Idea 01
How I got the idea

## Slide 5: The Laptop…
I found a laptop that we don’t use any more, So I thought of recycling it and giving it a new prepouse

## Slide 6: The Problems 02
The problems I faced during this project

## Slide 7: PROBLEMS BY TYPE SOFTWARE VS HARDWARE TIME TO FIX Under a day Multiple days CAUSES
60%
40%

## Slide 8: BIGGEST TIME SINKS 35% 40% 25%
Tracking down the PipeWire bug that sent audio out the wrong HDMI port
Getting the joystick reliably read as arrow keys under the Wayland compositor
Repairing the LCD panel after its LVDS connector latch broke

## Slide 9: COMPONENT ISSUES
WHAT WENT WRONG
COMPONENT | ISSUE
Joystick hole | Wrong HDMI port
Speaker grille | Both at once
Volume keys | Latch broke
COMPONENT | ISSUE
Audio output | Wider than screws
Volume knob | Size unconfirmed
LCD panel | Grabbed by OS

## Slide 10: FOUR MAIN PROBLEMS
mpv was sending sound out the wrong HDMI port
AUDIO ROUTING
The knob changed app and system volume together
VOLUME CONTROL
The connector latch snapped during repair
SCREEN CONNECTOR
Joystick hole ended up wider than its screws
HOLE VS SCREWS

## Slide 11: Solution of Problems 03
How I solved these problems

## Slide 12: HOW I FIXED THEM TOP FIX VOLUME AUDIO DEVICE KEY INPUT
mpv now points straight at the correct ALSA device
Checks the keysym and the raw hardware keycode both
Volume knob now calls wpctl to change the speaker

## Slide 13: DEBUGGING TOOLBOX
iptv-org database to verify channels
Round-trip tests before sending installer
wpctl status to check audio routing
key_debug.py to print real keycodes
Flashlight test for backlight vs video
BFS check for keyboard reachability
01
03
02
03
04
05
06

## Slide 14: WHERE THIS STANDS NOW
Software problems are fixed. Screen repair is in progress.

## Slide 15: The Wirring 04
How I wired the parts to the board

## Slide 16: WIRING OVERVIEW ARDUINO -> PI PI -> DRIVER BOARD DRIVER BOARD -> SCREEN JOYSTICK VOLUME KNOB POWER BUTTON
Connected over USB, sending plain text commands over serial
HDMI out from the Pi into the universal LCD controller board
LVDS ribbon cable plus a separate backlight power connector
Wired to Arduino digital pins for direction, plus one for the click button
A 10K potentiometer wired to an Arduino analog input
Its own Arduino digital pin, held for 2 seconds to shut down

## Slide 17: HOW A BUTTON PRESS TRAVELS 1. ARDUINO 2. THE BRIDGE 3. THE APP
Reads the joystick, knob, and button, and sends a plain text command over serial
rpi_bridge.py on the Pi turns that command into a real key or mouse event
tv.py receives it like any keyboard input and reacts on screen

## Slide 18: WIRING IN PROGRESS
Every input component runs back to the Arduino on its own pin, and the Arduino talks to the Pi over a single USB serial cable - no extra wiring needed between the controller and the software.

## Slide 19: FINISHED BUILD

## Slide 20: THREE MAIN CONNECTIONS USB SERIAL GPIO HDMI
Arduino to Raspberry Pi, carrying every joystick, knob, and button command
The power button wired straight to the Pi for a direct, reliable shutdown
Raspberry Pi to the driver board, carrying video to the recycled laptop screen

## Slide 21: WIRING REFERENCE TABLE
ARDUINO | Joystick X/Y/click | Knob wiper | Button pin
PI | USB from Arduino | HDMI to driver board | GPIO to power button
DRIVER BOARD | HDMI in | LVDS out to panel | Backlight power out
SCREEN | LVDS in | Backlight in | -
POWER | 5V to Pi | 12V to driver board | Shared ground

## Slide 22: BUILD MILESTONES Step 3 Step 4 Step 1 Step 2
PHASE 1
PHASE 2
Bridge turns serial into key events
Wire board and screen into case
Wire inputs to the Arduino
Flash sketch, test serial output

## Slide 23: Goals 05
What are my project’s goals.

## Slide 24: GOALS GOAL 1 GOAL 2
Build a fully working retro TV controllable end-to-end with just the joystick
Fit everything into a custom laser-cut enclosure sized for the recycled screen

## Slide 25: 264
Channels curated for the custom IPTV channel list, each checked twice before being added

## Slide 26: THANKS!
Do you have any questions?
youremail@freepik.com
+91 620 421 838
yourcompany.com
Please keep this slide for attribution