## Slide 1
RETRO TV
PROJECT
By Haidar Ali Alshowaikh | Class 8E

## Slide 2
WHAT IT'S BUILT FROM
Materials Used
Raspberry Pi
Arduino Uno
Potentiometer 10K
Jumper Wires
Button
Joystick Module
Old Laptop Screen
HDMI Module
02

## Slide 3
ROADMAP
What's Ahead
01
The Idea
How I got the idea
02
The Problems
What went wrong along the way
03
Solutions
How each problem got fixed
04
The Wiring
How every part connects
05
Goals
What the project set out to do
03

## Slide 4
SECTION 01
THE IDEA
How I got the idea
04

## Slide 5
SECTION 01 · THE IDEA
The Laptop...
I found a laptop that we don't use any more, so I thought of recycling it and giving it a new purpose.
05

## Slide 6
SECTION 02
THE PROBLEMS
What went wrong along the way
06

## Slide 7
SECTION 02 · THE PROBLEMS
Problems By Type
Chart: Software vs Hardware
| Software | Hardware
Share of problems | 60 | 40
TIME TO FIX
Under a day
Multiple days
07

## Slide 8
SECTION 02 · THE PROBLEMS
Biggest Time Sinks
35%
Tracking down the PipeWire bug that sent audio out the wrong HDMI port
40%
Getting the joystick reliably read as arrow keys under the Wayland compositor
25%
Repairing the LCD panel after its LVDS connector latch broke
08

## Slide 9
SECTION 02 · THE PROBLEMS
Component Issues
COMPONENT | ISSUE
Audio output | Routed to the wrong HDMI port
Volume knob | Changed app AND system volume at once
LCD panel | Connector latch broke during repair
Joystick hole | Wider than the module's own screws
Speaker grille | Size was an unconfirmed placeholder
Volume keys | Real multimedia keys grabbed by the desktop
09

## Slide 10
SECTION 02 · THE PROBLEMS
Four Main Problems
Audio Routing
mpv sent sound out the wrong HDMI port
Volume Control
The knob changed app and system volume together
Screen Connector
The connector latch snapped during repair
Hole vs Screws
Joystick hole ended up wider than its screws
10

## Slide 11
SECTION 03
SOLUTIONS
How each problem got fixed
11

## Slide 12
SECTION 03 · SOLUTIONS
How I Fixed Them
System Volume
Volume knob now calls wpctl to change the real speaker
Audio Device
mpv points straight at the correct ALSA HDMI device
Key Detection
Checks both the keysym and the raw hardware keycode
12

## Slide 13
SECTION 03 · SOLUTIONS
Debugging Toolbox
wpctl status
Check where audio was actually routing
key_debug.py
Print the real keycode for any key
Flashlight test
Tell a dead backlight from dead video
iptv-org
Verify channels before adding them
BFS check
Prove the keyboard is joystick-reachable
Round-trip test
Verify the installer before sending it
13

## Slide 14
SECTION 03 · SOLUTIONS
Where This Stands Now
Every major software problem has a working fix - audio, volume control, and key detection are all solid.
The screen connector repair is still in progress.
14

## Slide 15
SECTION 04
THE WIRING
How every part connects
15

## Slide 16
SECTION 04 · THE WIRING
Wiring Overview
Joystick
Arduino digital pins, plus one for the click button
Volume Knob
A 10K potentiometer on an Arduino analog input
Power Button
Its own pin, held 2 seconds to shut down
Arduino -> Pi
USB, sending plain text commands over serial
Pi -> Driver Board
HDMI into the universal LCD controller board
Board -> Screen
LVDS ribbon plus a separate backlight connector
16

## Slide 17
SECTION 04 · THE WIRING
How A Button Press Travels
1. ARDUINO
Reads the joystick, knob, and button; sends a command over serial
→
2. THE BRIDGE
rpi_bridge.py turns that command into a real key or mouse event
→
3. THE APP
tv.py receives it like normal keyboard input and reacts on screen
17

## Slide 18
SECTION 04 · THE WIRING
Wiring In Progress
Every input component runs back to the Arduino on its own pin, and the Arduino talks to the Pi over a single USB serial cable.
18

## Slide 19
SECTION 04 · THE WIRING
The Finished Build
19

## Slide 20
SECTION 04 · THE WIRING
Three Main Connections
USB Serial
Arduino to Pi, carrying every joystick, knob, and button command
GPIO
The power button wired straight to the Pi for a direct shutdown
HDMI
Pi to the driver board, carrying video to the recycled screen
20

## Slide 21
SECTION 04 · THE WIRING
Wiring Reference Table
 | PORT A | PORT B | PORT C
ARDUINO | Joystick X/Y/click | Knob wiper | Button pin
PI | USB from Arduino | HDMI to driver board | GPIO to power button
DRIVER BOARD | HDMI in | LVDS out to panel | Backlight power out
SCREEN | LVDS in | Backlight in | -
POWER | 5V to Pi | 12V to driver board | Shared ground
21

## Slide 22
SECTION 04 · THE WIRING
Build Milestones
STEP 1
Wire joystick, knob, and button to the Arduino
→
STEP 2
Flash the Arduino sketch, test raw serial output
→
STEP 3
Get rpi_bridge.py turning serial into key events
→
STEP 4
Wire the driver board, screen, and power button
22

## Slide 23
SECTION 05
GOALS
What the project set out to do
23

## Slide 24
SECTION 05 · GOALS
Goals
GOAL 1
Build a fully working retro TV, controllable end-to-end with just the joystick
GOAL 2
Fit everything into a custom laser-cut enclosure sized for the recycled screen
24

## Slide 25
264
Channels curated for the custom IPTV channel list, each checked twice before being added
25

## Slide 26
SECTION 06
PROJECT FAIR
How this project fits what judges look for
26

## Slide 27
SECTION 06 · PROJECT FAIR
Why This Fits The Fair
Real Problem Solved
Built a working alternative instead of buying a new TV
Engineering Process
Idea, problems, solutions, wiring, and testing - all documented
Sustainability
Gave a retired laptop screen a second life instead of e-waste
Original Build
Custom Arduino + Pi software, not an off-the-shelf kit
27

## Slide 28
SECTION 06 · PROJECT FAIR
Real-World Impact
Less E-Waste
One fewer laptop thrown out - the screen and body both got reused
Skills, Not Just Parts
Wiring, embedded software, and enclosure design in one build
Built To Show
Everything here actually works, live, not just on paper
28

## Slide 29
THANKS!
Haidar Ali Alshowaikh | Class 8E
YouTube @brackstudy
YouTube @brackstudy_arabic
Instagram @brackstudy
Instagram @brackstudy_arabic