## Slide 1
RETRO TV
PROJECT
By Haidar Ali Alshowaikh | Class 8E
BRACK STUDY TV
LIVE TV · TOD
APPS · APP STORE

## Slide 2
WHAT IT'S BUILT FROM
Materials Used
Replacement Pi 4
Arduino Uno
Volume knob
Speakers
Power button
Joystick Module
22-inch HDMI monitor
Enclosure frame
02

## Slide 3
ROADMAP
What's Ahead
01
The Idea
How I got the idea
02
The Problems
What went wrong along the way
03
Solutions
How each problem got fixed
04
The Wiring
How every part connects
05
Goals
What the project set out to do
03

## Slide 4
SECTION 01
THE IDEA
How I got the idea
04

## Slide 5
SECTION 01 · THE IDEA
The Monitor...
I reused an available monitor and built a new TV experience around it, with joystick controls and a retro-style cabinet.
05

## Slide 6
SECTION 02
THE PROBLEMS
What went wrong along the way
06

## Slide 7
SECTION 02 · THE PROBLEMS
Challenges Along the Way
TIME TO FIX
Under a day
Multiple days
07
SOFTWARE VS HARDWARE
HARDWARE
40%
SOFTWARE
60%

## Slide 8
SECTION 02 · THE PROBLEMS
Challenges That Took Work
INPUT
Making joystick navigation reliable on the Raspberry Pi
AUDIO
Routing sound to the right output and linking the knob to system volume
DISPLAY
Moving from the old laptop-panel setup to a 22-inch HDMI monitor
08

## Slide 9
SECTION 02 · THE PROBLEMS
Component Issues
COMPONENT | ISSUE
Audio routing | Audio initially went to the wrong output
Original Pi | Failed to boot; replaced with a Pi 4
Display setup | Current build uses direct HDMI
Cabinet frame | Frame is complete and reported good
Monitor choice | Changed to a 22-inch HDMI monitor
Desktop key handling | Desktop key handling needed a reliable fix
09

## Slide 10
SECTION 02 · THE PROBLEMS
Problems That Shaped the Build
Audio routing
Playback initially used the wrong output
Original Pi
Failed to boot; replaced with a Pi 4
Display setup
The current 22-inch monitor connects by HDMI
10

## Slide 11
SECTION 03
SOLUTIONS
How each problem got fixed
11

## Slide 12
SECTION 03 · SOLUTIONS
How I Fixed Them
System Volume
Volume knob now calls wpctl to change the real speaker
Audio Output
mpv uses the selected HDMI audio output
Key Detection
Checks both the keysym and the raw hardware keycode
12

## Slide 13
SECTION 03 · SOLUTIONS
Debugging Toolbox
wpctl status
Check where audio was actually routing
key_debug.py
Print the real keycode for any key
Flashlight test
Tell a dead backlight from dead video
iptv-org
Verify channels before adding them
BFS check
Prove the keyboard is joystick-reachable
Round-trip test
Verify the installer before sending it
13

## Slide 14
SECTION 03 · SOLUTIONS
Current Status
The latest update adds stream readahead and smoother player cleanup. Playback on the replacement Pi still needs testing to confirm the fix.
14

## Slide 15
SECTION 04
THE WIRING
How every part connects
15

## Slide 16
SECTION 04 · THE WIRING
Wiring Overview
Joystick
Arduino digital pins, plus one for the click button
Volume Encoder
The Uno sends volume-up and volume-down commands
Power Button
Connected directly to Pi GPIO3 and ground
Arduino -> Pi
USB, sending plain text commands over serial
Pi -> Monitor
HDMI cable carries video straight to the monitor
No driver board
The HDMI monitor has its own display electronics
16

## Slide 17
SECTION 04 · THE WIRING
How A Button Press Travels
1. ARDUINO
Reads the joystick, knob, and button; sends a command over serial
→
2. THE BRIDGE
rpi_bridge.py turns that command into a real key or mouse event
→
3. THE APP
tv.py receives it like normal keyboard input and reacts on screen
17

## Slide 18
SECTION 04 · THE WIRING
Wiring In Progress
The joystick and volume encoder connect to the Uno, which sends commands to the Pi over USB. The power button connects separately to GPIO3.
18

## Slide 19
SECTION 04 · THE WIRING
Build Status: Frame Complete
19

## Slide 20
SECTION 04 · THE WIRING
Three Main Connections
USB Serial
Arduino to Pi, carrying joystick and volume commands
GPIO
Power button wired to GPIO3 for safe shutdown
HDMI
Pi to the 22-inch HDMI monitor
20

## Slide 21
SECTION 04 · THE WIRING
Current Wiring Reference
 | PART | CONNECTION | PURPOSE
ARDUINO UNO | Joystick X/Y + click | Volume encoder A/B | USB serial to Pi
RASPBERRY PI | USB from Uno | HDMI to monitor | GPIO3 + GND to button
MONITOR | HDMI input | No LVDS connection | Monitor's own power
POWER BUTTON | Shutdown switch | GPIO3 + GND | Requests safe shutdown
POWER | USB-C to Pi | Monitor power cable | Uno powered over USB
21

## Slide 22
SECTION 04 · THE WIRING
Build and Test Flow
STEP 1
Connect joystick and encoder to the Uno
→
STEP 2
Flash the Uno and test USB commands
→
STEP 3
Set up the TV app and USB bridge on Pi
→
STEP 4
Connect HDMI monitor and test GPIO3 button
22

## Slide 23
SECTION 05
GOALS
What the project set out to do
23

## Slide 24
SECTION 05 · GOALS
Goals
GOAL 1
Build a retro TV prototype with joystick-led control
GOAL 2
Build a customer-sized cabinet around the chosen monitor
24

## Slide 25
264
in the current IPTV channel list; stream availability can change
25

## Slide 26
SECTION 06
PROJECT FAIR
How this project fits what judges look for
26

## Slide 27
SECTION 06 · PROJECT FAIR
Why This Fits The Fair
Real Problem Solved
Turned an available monitor into a useful TV
Engineering Process
A documented cycle of building, testing, and improving
Sustainability
Gave an unused display a new purpose and extended its useful life
Original Build
Custom Raspberry Pi TV app with Arduino controls
27

## Slide 28
SECTION 06 · PROJECT FAIR
Real-World Impact
Less E-Waste
An existing monitor now has a new purpose in a TV project
Skills, Not Just Parts
Wiring, embedded software, and enclosure design in one build
Built To Show
The TV app has stream readahead and cleanup updates. Playback tests on the replacement Pi are still pending.
28

## Slide 29
THANKS!
Haidar Ali Alshowaikh | Class 8E
YouTube @brackstudy
YouTube @brackstudy_arabic
Instagram @brackstudy
Instagram @brackstudy_arabic